RMRC – TAKEN FROM LAB 9
Defined the number of steps and the control frequency. Used epsilon value for damped least squares – value is from the tutorial. W is weighting matrix for velocity vector (first 3 for linear v x, y, z and last 3 for angular) – tute values again.
We didn’t calculate the angle error. Used jacob0 – jacobian with respect to base. If calculated manipulability is less than epsilon, recalculate for lambda, else lambda = 0.
If singularity is close to occuring during RMRC, the pathing will be sacrificed so that the robot avoids this singularity configuration.
Qwaypoints are basically q values for jacobian.
The jacobian indicates how the end effector will move as a function of the current joint state
To get the desired end effector velocity and I can compute the jacobian and invert it. I can work out what joint angle velocity I need to get to this desired end effector velocity.
Take the end effector desired velocity and multiply by the inverse jacobian to get the joint velocity we need. We move the robot at this joint velocity but after the robot has moved, q value changes, so we need to constantly update the jacobia matrix as we move the robot.
Go through the phase Moving the robot Joints, updating the Jacobian, computing the robot velocity, moving the robot joints, updating the jacobian…and so on.
At any given time, you can take the joint angles, compute the jacobian and take the inverse, then multiply by the desired velocity and compute the q values that are required for a given time. Then we take this new q values and time by a particular time to get the desired position of the joints and then we add that to the previous joint states which allows the robot to move to position that we would like at a particular time.
VISUAL SERVOING – POSITION OR VISUAL BASED – TAKEN FROM LAB 8
Space of the error is formulated in cartesian coordinates (3d points) OR in the image.
COLLISION DETECTION – TAKEN FROM LAB 5
Iterate through each of the joint positions. Used RectangularPrism function to create collision zones which returns rectangular vertices, faces and face normals. Use LinePlaneIntersection function which takes in the start and end point of a line segment and considers the face normal and vertices of the triangles. Use IsIntersectionPointInsideTriangle function to check if the point is actually inside triangle. If an intersection occurs, we move the joint cartesian position by a fixed value in the x, y and z direction. Screen will display “Avoiding Collision”.
DH PARAMETERS – they’re given by the company that manufactures the robot. They also provide the joint limits in their user guide
- d – perpendicular distance along the previous joints z axis to the common normal
- a – distance along the common normal
- alpha – change in angle from old z axis to new z axis between joints
- offset – rotation about z axis to align x axis to new x axis
FORWARD KINEMATICS – used to calculate position of end effector with respect to joint angles. Used it in the end effector xyz jogging. Used it to get the xyz coord of end effector and then either increment or decrement from that current value.
INVERSE KINEMATICS – used to calculate joint angles with respect to a predetermined end effector positions. Also used in jogging to calculate joint angles for the desired xyz end effector position. We used ikcon to include the joint limits in the jogging.
CODE STRUCTURE – Define can starting coorinates. Create respective transforms. Generate can in environment. Get user to select which can is to be on top shelf. Create collision objects in environent. Redefine can starting pos. Define sequence RPY values for respective waypoints. Move robot to starting pos (q0). Define waypoints. Animation: Iterate through joints to check collision. If collision occurs, adjust. Perform RMRC and move to first waypoint and set endeffector RPY. Animate to waypoint. Check for collisions again. It’s set out so the robot is animating the can in the end effector when the sequence number increments.